## Slide 1
3UK 4G Ericsson WP6 Daily Performance Report
Ericsson NPO
03/12/2021

## Slide 2: Summary
Data Availability:
4G (Ericsson) 03rd Nov till 07:00
Observed sudden spike in Volte DCR. And We Observed continuous Degradation in the site-NOT213 for the KPI's LTE Drop rate in the Cell A61 since 17/11/2021 9:00-Hr. This impacting site is the reason for Network level change. Captured under #INC300000741666
4G-4G Data HOSR has degraded on 23rd November 00:00Hrs onwards. Around 28 sites were impacted data HOSR on 23rd of November.. After analysis found traffic has increased due to multiple football events were held on the same day. 1. Chelsea vs Juventus. UEFA Champions League Group H at Stamford bridge Stadium.
Volte DCR has degraded on 22nd November. After analysis found 2 sites were impacting the entire Network very badly MAN442BB1 and SFD111E.
Most of the KPI has degraded at 8PM on Wednesday as we had a football match between PSG Vs MAN City at Manchester after KPIs is in normal trend
Volte attempts and volte traffic has degraded on Wednesday as we had Maya Core issue :- Support observed a 58% traffic reduction on 4G incoming calls routing towards the Maya network from Legacy. Nokia confirmed that there were no call failures on the Maya network as the calls were falling back to 3G as confirmed by Legacy support. (approx. 10,000 per minute). There was a small degradation being observed on 3G voice. Approx. 0.55% (260 3G calls failing per minute out of a total 36,764).
Volte DCR has degraded on 26th 00:01 Hrs, Later back to normal from next ROP. Observing KPI LTE_Data_Drop rate got continues degrading in the site MAN442 in the cell-C53 since 21/11/2021 12:00-Hrs which is top impacting site. Captured under #INC300000748254
4G-4G Data HOSR has degraded during weekends . After analyzing we found that SHF300 site failing in preparation phase towards the target site RHM019 as this site is facing availability issue ( Site down) . Still degrading. captured under # INC300000749706
PS IRAT SR Has slightly degraded at 03:00Hrs on 30th November. Last ROP seems back to normal.
Volte DCR has degraded on 01/12/2021 00:00Hrs onwards, LCR171 is the site was top impacting ( B62) . Now trending back to normal.
Observations:
3UK
Ongoing Analysis:
We have seen impact towards DATA And Voice Accessibility due to core issue since 03/12/2021 06:15 onwards & restored 07:15. Captured under # INC754608, #INC300000754416, #INC300000754165, #INC300000754416 and #INC300000754602
.

## Slide 3: 3UK 4G Network Level Performance Stats
Chart: 4G Data Accessibility
Week 49 | 99.92 | 99.91 | 99.86 | 99.89 | 99.9 | 99.84 | 99.91 | 99.85 | 99.8 | 99.83 | 99.89 | 99.84 | 99.85 | 99.86 | 99.85 | 99.85 | 99.84 | 99.85 | 99.82 | 99.85 | 99.88 | 99.86 | 99.92 | 99.93 | 99.87 | 99.93 | 99.92 | 99.89 | 99.95 | 99.96 | 99.95
Chart: LTE Data Retainability
Week 49 | 99.01 | 99.08 | 99.13 | 99.14 | 99.12 | 99.07 | 98.92 | 98.73 | 98.47 | 98.5 | 98.44 | 98.38 | 98.28 | 98.28 | 98.38 | 98.29 | 98.38 | 98.36 | 98.44 | 98.55 | 98.6 | 98.73 | 98.82 | 98.87 | 98.99 | 99.15 | 99.11 | 99.26 | 99.28 | 99.28 | 99.2
Chart: VoLTE DCR
Week 49 | 1.43 | 1.72 | 1.69 | 1.26 | 0.94 | 0.89 | 0.75 | 1.36 | 1.24 | 1.41 | 1.22 | 1.38 | 1.67 | 2.08 | 1.61 | 1.45 | 1.7 | 1.95 | 1.77 | 1.92 | 1.74 | 1.94 | 1.73 | 1.73 | 3.66 | 1.48 | 3.42 | 0.63 | 1.29 | 0.85 | 0.81
Chart: VoLTE Accessibility
Week 49 | 99.84 | 99.81 | 99.71 | 99.8 | 99.71 | 99.62 | 99.81 | 99.78 | 99.74 | 99.74 | 99.8 | 99.72 | 99.75 | 99.77 | 99.73 | 99.76 | 99.73 | 99.75 | 99.69 | 99.79 | 99.82 | 99.71 | 99.82 | 99.71 | 99.76 | 99.84 | 99.86 | 99.86 | 99.85 | 99.94 | 99.82
Trends produced by taking BIS’ed sites
Volte DCR has degraded on 26th 00:01 Hrs, Later back to normal from next ROP. Observing KPI LTE_Data_Drop rate got continues degrading in the site MAN442 in the cell-C53 since 21/11/2021 12:00-Hrs which is top impacting site. Captured under #INC300000748254

## Slide 4: 3UK 4G Network Level Performance Stats
Chart: 4G – 4G Voice Handover
Week 49 | 99.58 | 99.67 | 99.63 | 99.7 | 99.63 | 99.71 | 99.64 | 99.56 | 99.48 | 99.47 | 99.44 | 99.39 | 99.36 | 99.33 | 99.36 | 99.36 | 99.34 | 99.32 | 99.28 | 99.32 | 99.33 | 99.35 | 99.43 | 99.51 | 99.61 | 99.68 | 99.68 | 99.67 | 99.74 | 99.65 | 99.7
Chart: SRVCC Handover SR
Week 49 | 90.8 | 97.5 | 100 | 88.24 | 100 | 100 | 100 | 96.07 | 96.22 | 94.77 | 96.8 | 91.57 | 94.07 | 95.14 | 94.79 | 92.79 | 92.95 | 95.36 | 95.45 | 95.08 | 93.17 | 90.1 | 93.81 | 94.48 | 93.2 | 97.56 | 100 | 100 | 100 | 100 | 97.44
Chart: 4G – 4G Data Handover
Week 49 | 99.02 | 98.22 | 97.59 | 98.74 | 96.55 | 99.08 | 99.15 | 97.29 | 97.88 | 96.82 | 96.25 | 93.79 | 96.67 | 96.77 | 96.95 | 97.77 | 98.42 | 98.55 | 98.57 | 98.62 | 98.66 | 98.31 | 98.84 | 98.79 | 98.05 | 98.92 | 99.08 | 96.44 | 99.32 | 99.15 | 99.26
Chart: PS IRAT Handover SR
Week 49 | 94.17 | 97.25 | 95.53 | 93.92 | 96.64 | 94.55 | 94.23 | 94.05 | 94 | 94.42 | 94.63 | 94.76 | 94.14 | 93.67 | 93.73 | 93.88 | 93.17 | 92.4 | 91.29 | 92.56 | 91.67 | 91.59 | 90.65 | 91.5 | 93.74 | 94.06 | 96.29 | 96.2 | 97.25 | 96.88 | 96.01
Trends produced by taking BIS’ed sites
4G-4G Data HOSR has degraded during weekends . After analyzing we found that SHF300 site failing in preparation phase towards the target site RHM019 as this site is facing availability issue ( Site down) captured under # INC300000749706
Most of the KPI has degraded at 8PM on Wednesday as we had a football match between PSG Vs MAN City at Manchester after KPIs is in normal trend

## Slide 5: 3UK 4G Network Level Performance Stats
Chart: VoLTE traffic
Week 49 | 40.97 | 24.32 | 13.52 | 8.4 | 5.6 | 5.75 | 11.21 | 32 | 87.5 | 136.16 | 156.24 | 166.94 | 176.1 | 175.29 | 186.24 | 197.73 | 199.94 | 197.93 | 171.29 | 150.16 | 138.39 | 123.3 | 94.75 | 61.62 | 40.62 | 25.19 | 13.66 | 7.9 | 5.79 | 6.23 | 7.62
Chart: VoLTE Attempts
Week 49 | 9338 | 5102 | 3253 | 2176 | 1958 | 3156 | 6747 | 20639 | 58687 | 62169 | 68796 | 75027 | 79958 | 83113 | 87837 | 103816 | 95409 | 86242 | 72597 | 60170 | 48439 | 37249 | 25559 | 15539 | 8865 | 4752 | 2957 | 1740 | 1918 | 3257 | 4566
Chart: UserThruDataDL(Mbps)
Week 49 | 39.64 | 47.06 | 54.98 | 61.17 | 63.94 | 64.28 | 55.81 | 45.32 | 37.08 | 36.32 | 33.84 | 31.14 | 29.6 | 29.21 | 29.27 | 27.68 | 26.69 | 25.82 | 26.98 | 27.28 | 26.87 | 26.69 | 28.7 | 34.15 | 41.67 | 49.35 | 54.84 | 61.37 | 61.59 | 61.03 | 57.19
Chart: Total Data Vol(Gb)
Week 49 | 3944.11 | 3006.05 | 2263.45 | 1716.14 | 1382.42 | 1308.66 | 1554.47 | 2296.41 | 3044.09 | 3214.68 | 3546.52 | 3777.65 | 4185.1 | 4267.17 | 4312.08 | 4728.66 | 5002.55 | 5287.57 | 5489.67 | 5732.53 | 5946.18 | 5879.67 | 5489.4 | 4666.31 | 3772.39 | 2837.2 | 2190.55 | 1770.37 | 1402.31 | 1305.72 | 1093.83
Trends produced by taking BIS’ed sites
Volte attempts and volte traffic has degraded on Wednesday as we had Maya Core issue
Volte attempts and volte traffic has degraded on Wednesday as we had Maya Core issue

## Slide 6
Thank You